GAMMA COOL BOX

BILL OF MATERIAL

June 2018, by Mej

| TOTAL |  | 236 € |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Ref | Details | Unit cost | Quantity | Total cost |
|  |  |  | [€] |  | [€] |
| Modules |  | 124 € |  |  |  |
| Fan+Radiator | GAMMAX_200 | 12V, 200mA | 12.0 € | 5 | 60 € |
|  |  | 4pin connector |  |  |  |
|  |  | 95W |  |  |  |
|  |  | 30dB |  |  |  |

| Peltier | TEC1-07108HT | 30x30x3.5mm | 5.0 € | 2 | 10 € |
| --- | --- | --- | --- | --- | --- |
|  |  | 8.5V/8.5A |  |  |  |

| Peltier | TES1-3105 | 15x15x5mm | 3.0 | € | 2 | 6 | € |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 3.5V/5A |  |  |  |  |  |
| Power supply | RS-150-12 | Input: 88-264V / 47-63Hz | 34.0 | € | 1 | 34 | € |
|  |  | Output: 12V / 12.5A (150W) |  |  |  |  |  |
|  |  | 199x98x38mm |  |  |  |  |  |
|  |  | ! Without cable ! |  |  |  |  |  |
| DC/DC buck | LM2596 module | Step-down. 3A max | 2.0 | € | 1 | 2 | € |
|  |  | Manual potentiometer |  |  |  |  |  |
|  |  | IC alone cost 3-4€ per 10 on elec |  |  |  |  |  |
|  |  | suppliers… |  |  |  |  |  |
| MCU | Arduino Leonardo | ATmega32U4 | 10.0 | € | 1 | 10 | € |
|  |  | 5V/16MHz |  |  |  |  |  |
|  |  | Native USB core |  |  |  |  |  |
|  |  | 60kHz 8 bit PWM |  |  |  |  |  |
| RF | NRF24L01 module | RF module compatible MCU Arduino | 2.0 | € | 1 | 2 | € |

|  | Ref |  | Details | Unit cost |  | Quantity | Total cost |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | [€] |  |  | [€] |
| Drivers |  | 16 € |  |  |  |  |  |
| Dual Full-Bridge | DRV8432 |  | GND to Vcc output (Vcc = 12V) | 5.6 | € | 1 | 6 € |
|  |  |  | 7A/channel, 12A peak |  |  |  |  |
|  |  |  | PWM ctrl |  |  |  |  |
|  |  |  | Custom SSOP (14x16mm_Pitch0.65mm) |  |  |  |  |
| L | DENO-23-0001 |  | 2000uH - 16A max | 1.0 | € | 2 | 2 € |
|  |  |  | NOT shielded |  |  |  |  |
|  |  |  | TH, Ø23mm |  |  |  |  |
| Dual Full-Bridge | DRV8412 |  | GND to Vcc output (Vcc = 12V) | 3.5 | € | 1 | 4 € |
|  |  |  | 3A/channel, 6A peak |  |  |  |  |
|  |  |  | PWM ctrl |  |  |  |  |
|  |  |  | HTSSOP-44-EP (8x14mm_Pitch0.635mm) |  |  |  |  |
| L | HCTI-330-5.2 |  | 330uH - 5.2A max | 1.2 | € | 2 | 2 € |
|  |  |  | shielded |  |  |  |  |
|  |  |  | TH, Ø32mm |  |  |  |  |
| Single bridge | DRV8830 |  | 0.5V to 5V ouput (Vcc=6V) | 1.0 | € | 2 | 2 € |
|  |  |  | 1A max, 1.5A peak |  |  |  |  |
|  |  |  | I²C com |  |  |  |  |
|  |  |  | MSOP-10 (5x3mm_Pitch0.5mm) |  |  |  |  |
| Other ICs |  | 8 € |  |  |  |  |  |
| GPIO Expender | PCA9555 | SOIC-24 | 16 GPIO expender, I²C com | 0.9 | € | 1 | 1 € |
|  |  |  | 7.5x15.4mm_Pitch1.27mm |  |  |  |  |
| I²C Fan controler | MAX31790 | QFN-28-1EP | 6 channel "4 pin fan" controler | 2.4 | € | 1 | 2 € |
|  |  |  | 4x4mm_Pitch0.4mm |  |  |  |  |
| I²C Temp sensor | MCP9904T-A | VDFN-10 | 1 internal + 3 outside junction sensor | 0.7 | € | 5 | 4 € |
|  |  |  | 3x3mm_Pitch0.5mm |  |  |  |  |
| LDO 5V | MIC5219 | SOT23-5 | 3.3V/500mA, Vin=10V max | 0.6 | € | 1 | 1 € |
| LDO 3.3V | MIC5504 | SOT23-5 | 3.3V/300mA, Vin=5.5V max | 0.6 | € | 1 | 1 € |
| Passive electronic |  | 6 € |  |  |  |  |  |
| Connector | 2x4 SMD |  |  | 0.20 | € | 12 | 2 € |
|  | 1x4 SMD |  |  | 0.10 | € | 6 | 1 € |
|  | Bornier SMD |  | 9A | 0.50 | € | 2 | 1 € |
| Q |  |  | for thermal sensing | 0.05 | € | 15 | 1 € |
| LED |  | 1206 |  | 0.05 | € | 14 | 1 € |
| R |  | 1206, 0805 |  | 0.01 | € | 53 | 1 € |
| C |  | 1206, 0805, 0603 |  | 0.01 | € | 40 | 0 € |
| Raw stock |  | 68 € |  |  |  |  |  |
| Aluminium |  | 10mm |  |  |  |  | 50 € |
| Wood |  | 18mm |  |  |  |  | 10 € |
| Blue Foam |  | 80mm |  |  |  |  | 5 € |
| FR4 PCM |  | 1.6mm, 35µm Cu |  |  |  |  | 3 € |
| Miscellaneous |  | 14 € |  |  |  |  |  |
| Wires |  | 200mm, female, Pitch2.54mm |  | 0.05 | € | 28 | 1 € |
| USB Cable |  |  |  | 1 | € | 1 | 1 € |
| power cable |  |  |  | 1 | € | 1 | 1 € |
| Screws |  | M3, 22mm |  | 0.05 | € | 20 | 1 € |
| Thermal paste |  | 15cc syringe |  | 5 | € | 1 | 5 € |
| Soldering paste | Quickchip | 15cc syringe, 220°C |  | 5 | € | 1 | 5 € |