Laser sensors

M18 tubular housing

Max. range 60 m

Class 1 laser

|  | Top five product features! |
| --- | --- |
|  | • Class 1 laser light source detects small objects and |
|  | provides visual indication of beam alignment |
| 72 mm | • 316 stainless steel housing designed and tested to |

withstand industrial automation applications

• Extremely long sensing ranges for application flexibility

• Innovative two-pushbutton ‘Teach Mode’ offers simple adjustment for quick setup

• Flexible mounting bracket system simplifies installation

Class 1 laser sensors detect small parts at long distances

Laser sensors are used where detection of small objects or precise positioning is required. Laser light consists of light waves of a single wavelength, high in energy and power density because the waves are in phase with each other. This results in a tightly focused, almost parallel light beam that can detect very small objects at long ranges.

An important feature of the laser is that the light beam is visible, and during set-up of the sensor, the laser power is increased. This provides a bright light spot clearly visible even in the daylight which aids alignment. ifm efector also offers fine adjustment mounting brackets that allow the laser sensors to be precisely aligned for optimum performance.

The OG Series laser sensors are listed as FDA Class I Laser Products and comply with the nternationali standard IEC60825 and European standard EN60825 which describe the opera-tion of laser sensors.

Innovative teach mode

The innovative teach mode eliminates complex programming. The sensor features one button each for teaching a precise on and off state for the sensor signal.

PNP to NPN converter cordset

This cordset converts PNP outputs to NPN outputs.

Part no.: EVC01E (5 meters)

List price (1-pc): $19.00

Laser sensors

| Product + accessory selector |  |  |  |  |
| --- | --- | --- | --- | --- |
| Function | Range | Output | Spot Ø at | Supply | Switching | Light | Part | List Price |
|  |  |  | max range | Current | Frequency | Source | No. | (1-pc.) |
| Diffuse background | 20...200 mm | LO/DO PNP | 1.2 mm | 15 mA | 1000 Hz | Class 1 laser | OGH700 | $244.00 |
| suppression |  |  |  |  |  |  |  |  |
| Polarized | 0.2...15 m | LO/DO PNP | 40 mm | 15 mA | 2000 Hz | Class 1 laser | OGP700 | $241.00 |
| retro-reflective | 0.2...2 m | LO/DO PNP | 5 mm | 15 mA | 2000 Hz | Class 1 laser | OGP701 | $241.00 |
| Thru-beam | 0...60 m | LO/DO PNP | – | 11 mA | 1000 Hz | Class 1 laser | OGE700 | $131.00 |
| receiver | 0...2 m | LO/DO PNP | – | 11 mA | 1000 Hz | Class 1 laser | OGE701 | $131.00 |
| Thru-beam | 0...60 m | – | 150 mm | 13 mA | – | Class 1 laser | OGS700 | $189.00 |
| transmitter | 0...2 m | – | 5 mm | 13 mA | – | Class 1 laser | OGS701 | $189.00 |
| Optional Accessories |  |  | Cordsets |  |  |  |  |
| Type | Description | Part | List Price | Type | Description | Part | List Price |
|  |  | No. | (1-pc.) |  |  | No. | (1-pc.) |
| Fine adjust swivel bracket for OG laser | E20987 | $45.00 |  | M12 Micro DC (4-pin) 2 m, PUR | EVC001 | $9.95 |
|  |  |  |  |  | M12 Micro DC (4-pin) 5 m, PUR | EVC002 | $13.50 |
| Rail mount package, fine adjust swivel | E20868 | $54.00 |  |  |  |  |  |
|  | bracket for OG laser |  |  |  | M12 Micro DC (4-pin) 2 m, PUR | EVC004 | $9.95 |
|  | 10 x 50 mm reflector | E20988 | $16.00 |  | M12 Micro DC (4-pin) 5 m, PUR | EVC005 | $13.50 |
|  | 50 x 50 mm reflector | E20722 | $15.00 |  | M12 Micro DC (4-pin) 2 m, PUR, LED | EVC007 | $12.75 |
|  | 10 mm reflector | E20990 | $12.00 |  |  |  |  |  |
|  | 19 mm reflector | E20993 | $12.00 |  | M12 Micro DC (4-pin) 5 m, PUR, LED | EVC008 | $15.00 |
| Can’t find the right sensor for your application, call 800-441-8246 or visit www.ifm.com/us |  |  |  |

Technical Specs

| Supply voltage: | 10...36 VDC |  |
| --- | --- | --- |
|  |  | CLASS 1 |
| Light source: | Red light 655 nm |  |
| No. of wires: | 3-wire | LASER |
|  |  | PRODUCT |
| Maximum load current: | 200 mA |  |
|  |  | IEC60825-1:2007 |
| Voltage drop: | <2.5 V | 21CFR PART1040 |
| Leakage current: | Negligible |  |
| Connector: | M12 | Class 1 Laser |
| Housing material: | 316 stainless steel |  |
| Lens material: | PMMA |  |
| Operating temperature: | 14...140 °F (-10...60 °C) |  |
| Protection: | IP67 |  |

Dedicated sales engineers

ifm’s experienced sales engineers understand

your applications and provide solutions to

your challenges.

Place orders, tech support

800-441-8246

Visit our product catalog

www.ifm.com/us

Shop for products online

Easy ordering via eShop